## Slide 1: Safe and Efficient Reinforcement Learning for Frequency Control
Baosen Zhang
ECE, University of Washington
Joint work with Wenqi Cui
NREL Workshop on Resilient Autonomous Energy Systems
Sept 9th, 2021

## Slide 2: Changing Grid
Fundamentally changes how we think about the grid
We will talk about frequency stability
Johnson, 19

## Slide 3: Machines to Electronics
Not Sustainable
Sustainable
Hundreds of generators
Large mechanical inertia
Slow and inflexible control
Millions of devices
Less stored energy
Fast and flexible control
Tamrakar, 17
High Inertia
Low Inertia
+
+
-
-
+
-

## Slide 4: Performance Degradation
Nordic system: disturbances with frequencies under 49.7 Hz due to an N-1 contingency.
[Winter et al. IEEE Power & Energy Magazine ‘15]
Nine of the 13 wind farms online did not ride through … during the event

## Slide 5: Frequency Response
Synchronous generators follow negative linear feedback control
Linear droop control
Generator
K

## Slide 6: Frequency Response
Linear control law may not be optimal
Inverters can realize almost arbitrary control laws
Synchronous machines
Stable
Low cost

## Slide 7: Challenges
Inverter
Power System
Non-linear
swing dynamics
t
0
t
0
u
Cost on frequency deviation
Cost on control effort
+
Local measurement

## Slide 8: Contributions
A way to design nonlinear controllers
Guarantee stability by construction using Lyapunov theory
Better performance than the linear ones
Fast training
(b) Structure of the Stabilizing Controller
(a) Power Grid
(c) RNN based Framework for Efficient Training

## Slide 9: Swing Equations
Angle
Frequency
State Variables
Inertia constant
Power flow between line (i,j)
Static controller that change active power for primary frequency regulation
Net power injection
Conventional linear droop:
Inverter: to be designed

## Slide 10: Optimization Problem
Minimizes max frequency deviation and control effort
Nonlinear and nonconvex problem over a functional space
The stability constraint is hard to deal with
Using machine learning?

## Slide 11: Naïve Learning Approach
Parametrize the controller as a neural network
Can run something like RL
Standard algorithms: update NN parameters to minimize cost
power system
initialization
time-domain
simulation
cost
NN Controller

## Slide 12: Naïve RL Approach
Testing results
Average batch loss along episodes
Neural network controller
Learned by RL
Unstable behavior

## Slide 13: Stability Constraints
power system
initialization
time-domain
simulation
cost
NN Controller

## Slide 14: Lyapunov Functions
Stability roughly means that the total energy in the system should decrease
Formalized by Lyapunov functions
If V exists, all trajectories go to the equilibrium
Dynamical system
Scalar valued function
Positive Definite
Dissipative

## Slide 15: How do you find V?
Typically, a very hard problem for nonlinear systems
Decades of research into Lyapunov functions for power systems

## Slide 16: Energy Functions
Well-known energy function:
Not quite a Lyapunov function, it’s not lower bounded
Good enough for angles between -90 to 90 degrees
Kinetic Energy
Potential Energy
Varaiya, Wu, Sastry, Bergen, Pai, Chiang, Vittal, Sauer,…

## Slide 17: Lyapunov Conditions
Positive Definiteness
Dissipative

## Slide 18: Controller Constraints
Controllers are (locally) exponentially stable if
has the same sign as
is monotonic
Plus, the saturation constraints:
These are algebraic constraints on the function u

## Slide 19: Controller Constraints
These conditions translate to satisfies:
crosses the origin, increasing
Clip the output to satisfy power constraints

## Slide 20: Neural Network Structure
power system
initialization
time-domain
simulation
cost
NN Controller

## Slide 21: Neural Network Structure
ReLU layer

## Slide 22: Training
Discrete time system for training
The parameterized controller shows up at all timesteps
Straightforward gradient update is inefficient
power system
initialization
time-domain
simulation
cost

## Slide 23: RNN for Training
About 75% reduction in training time
Integrate state transition dynamics in recurrent neural network (RNN)
  Define the cell states to be and
  Operation of cell unit follows the swing equation
swing equations

## Slide 24: Simulation Setup
Added some inverter-based resources
Random initialization and step disturbances
Performance metric: max frequency deviation and control effort
IEEE 39 bus system

## Slide 25: Full Machine and Power Electronics Models

## Slide 26: Simulation Results
Cost vs variations in initialization
Example control laws

## Slide 27: Training Time
From a cold start, takes about 12 minutes to train the controller for the 39-bus system
300-bus system: about 14.5 minutes to train
Warm start helps quite a bit
Cold Start
Linear
Warm Start

## Slide 28: Robustness
Topology changes often in real systems
  Planned and unplanned outages
step disturbance
line outage

## Slide 29: Robustness
Stability conditions do not depend on topology
Optimality does
Positive Definiteness
Dissipative

## Slide 30: Questions
We used lossless power flow equations
Real system have (small) losses
No energy functions for lossy networks
Use learning to augment the previous Lyapunov function
lossy power flow

## Slide 31: Future Questions and Conclusion
Other control problems
Understanding robustness and perturbations
Stability doesn’t imply hard constraint satisfaction
Summary:
Learning can solve hard problems
Physical constraints makes the problem easier and more interesting